## Slide 1: Intravenous Sedation Monitoring
Saturday 4th October
1.45- 3.00
Helen McGreevy

## Slide 2: Aims
To understand clinical monitoring
To know how electromechanical monitoring works
Monitoring blood pressure

## Slide 3: Learning Outcomes
GDC Development outcome C
NEBDN Conscious Sedation for Dental Nurses 3.5.7,8 & 9,

## Slide 4: Monitoring
Why?
Sedation reduces perception
Enhances safety by recognising an early incident
Allows intervention & correction of a problem before injury
Minimises patient risk

## Slide 5: Monitoring
Clinical Observation and Monitoring, this is you!
Electromechanical Monitoring.

## Slide 6: Clinical Monitoring
Patient responses
Breathing
Colour of skin and mucosa
Patient movements
Sounds

## Slide 7: Clinical monitoring
Pulse
Breathing
Rate: 10– 15 breaths minute
Rhythm: regular
Depth: 0.5cm – 1cm
Mirror misting

## Slide 8: Clinical Monitoring
Colour
Pale: Faint, respiratory
depression
Red: Warm, allergy, choking
Blue: cold, cyanosis
Grey: MI, pain

## Slide 9: Clinical monitoring
Movements
Eye movements
Tongue movements
Muscle tone e.g. hands
Chest movements

## Slide 10: Clinical monitoring
Sounds
Snoring: obstruction of pharynx by
tongue
Gurgling: foreign matter in upper airway
Crowing: partial laryngeal obstruction
Wheezing: lower airway obstruction
Silence: total laryngospasm

## Slide 11: Clinical monitoring Check the pulse!
How many do you know of?
Temporal
Facial labial
Carotid
Radial
Femoral

## Slide 12: Pulse, What is it?
A pulse is a rhythmical throbbing of the arteries as blood is pumped through them.
We monitor the pulse during conscious sedation to allow us to compare should a complication arise. Monitoring the pulse will tell us what the heart is doing and how well it is performing.
The information a pulse provides is the ‘Beats Per Minute’. (bpm)
The medical terminology for a slow pulse rate is – Bradycardia
The medical terminology for a fast pulse rate is - Tachycardia

## Slide 13: Where do I find a Pulse?
Notes: Radial, brachial, temporal, carotid

## Slide 14
The Facial Labial pulse can be located in the lower border of the mandible, near the anteroinferior angle of the masseter muscle. This pulse is a branch of the facial artery which supplies blood to the lips and is easily palpable in this area.

## Slide 15: Normal Pulse Rates
Newborn baby -100-180 bpm
Infant – 80-150 bpm
Child age 2-6 –75-120 bpm
Child age 6-12 –70-100 bpm
Adolescent to Adult – 60-80 bpm
The normal pulse rate for an adult at rest is 72bpm
Notes: What pulse should be taken during a patient's treatment pathway with conscious sedation? |Radial pulse

## Slide 16: Clinical Monitoring
For inhalation sedation only clinical
monitoring mandatory
Blood pressure monitoring and
pulse oximetry is good practice
For Intravenous sedation electromechanical monitoring is essential

## Slide 17: Clinical Monitoring
Respiration is the rate at which a person inhales and exhales. It is usually measured to obtain a quick evaluation of a person’s health.
After taking a patient’s pulse, the rise and fall of the chest should be observed and counted for 30 seconds with the number of cycles being doubled.
What is a cycle? It is the rise, fall and brief pause of the chest.
The medical terminology for slow breathing is Bradycardia.
The medical terminology for fast breathing is Tachycardia.

## Slide 18: Respiration Rates
Newborn baby – 30 – 50 rpm
Child 2 – 12 years – 20 – 30 rpm
Teenage 12 – 17/18 – 12 – 20 rpm
Adult – 12 – 18 rpm
The abbreviation for respirations per minute is RPM

## Slide 19: Level of Consciousness
It is important to monitor a patient’s level of consciousness when receiving conscious sedation because the drugs and techniques used to provide conscious sedation for dental treatment should carry a margin of safety wide enough to render loss of consciousness unlikely.
Factors to be monitored include:
Is the patient responding?
What does their complexion, skin tone look like?
Pulse and respiratory rates
Notes: Discuss Height, weight and temperature

## Slide 20: Electromechanical monitoring
Pulse oximetry and oxygen saturation
Non-invasive blood pressure monitoring

## Slide 21: Pulse Oximetry
Measures arterial oxygen saturation & pulse
Peripheral tissues ( finger / ear lobe)
Detects and quantifies hypoxaemia
Non-invasive
Continuous monitoring
Early warning

## Slide 22: Pulse Oximeter

## Slide 23: Pulse Oximetry
This Photo by Unknown Author is licensed under CC BY

## Slide 24: Pulse Oximetry
Small changes in % saturation
mean large changes of partial pressure
Normal healthy pt. SaO2 -> 97 %
Sedated patient. SaO2 >90%
Clinical cyanosis SaO2 70 –
75%

## Slide 25: Pulse Oximetry
Saturation may drop dramatically over first 10 – 15minutes
If saturation <95%
Encourage deep breathing
Provide supplemental O2 (1-2 L per min)
Airway management

## Slide 26: Pulse Oximetry (Alarms)
Saturation 90% - 94%
Heart rate High 130 bpm
Low 50 bpm
Notes: These can be set by your clinician

## Slide 27: Blood pressure
Blood pressure measurement is mandatory
Preoperative BP
Administration of midazolam can lead to hypotensive episodes
Postoperative BP

## Slide 28: Blood pressure
Intraoperative BP?
For IV sedation this must include the appropriate use of pulse oximetry and blood pressure monitoring”
Notes: Intraoperative blood pressure refers to monitoring and maintaining blood pressure to prevent any type of organ injury. High and low bp can both cause harm with sever or prolonged hypotension linked to myocardial injury, acute kidney injury and death. Hypertension can also be harmful causing the same injurys.

## Slide 29: What is Blood Pressure?
Blood pressure is the force per unit area exerted on the wall of a blood vessel by the blood.
What determines a patient’s blood pressure? The force that is used to push the blood through the veins every time the heart beats and rests. If the heart pumps more blood through the arteries, or they are narrowed and stiff, the arteries will resist the blood flow. This results in the blood pressure being raised and if less blood is pumped through the arteries, or they are larger and more flexible, blood pressure will be lower.

## Slide 30: What does the Blood Pressure measure?
The Heart
At its highest – Systolic
At its lowest - Diastolic

## Slide 31: What happens within the Heart?
The left ventricle pumps blood into the aorta. The aortic walls stretch to allow the increased volume of blood received and the heart is at its highest pressure to provide the systolic reading. The aortic walls start to recoil, pushing blood into the arteries ensuring an onward flow. The heart at this stage is between beats. The aortic valve then closes as the pressure exceeds that of the left ventricle to prevent a backflow of blood. As the aorta and artery walls return to normal, the pressure drops to its lowest, prior to the next beat, which provides the diastolic reading.

## Slide 32: Knowledge Test
What does blood pressure measure?
How is blood pressure recorded?
What equipment is required to take a manual blood pressure?
Can blood pressure vary from appointment to appointment?
What is normal blood pressure?
Which of the two figures recorded are of concern if elevated?

## Slide 33: Answers
The heart at it highest and lowest
Systolic over Diastolic
Stethoscope and sphygmomanometer
Yes, as a person’s blood pressure changes constantly to meet the demands of the body
110/70 or 120/80
The diastolic, as it reflects the heart at its lowest pressure

## Slide 34: Questions?